## Slide 1: Evolving Automation Using SpatialAnalyzer
Ray Ryan
VP

## Slide 2: OUTLINE
Varying Degrees of Automation
  SA Functions
  MP/Scripts
  Operator Assisted Process
  Fully Automated Process
Examples
  Relationships for LLNL-NIF
  MPs for Data Management - NIST
  Tool Recertification on A350
  Fuselage Assembly on Global 7000

## Slide 3: Varying Degrees of Automation
Simplest – SA Functionality (i.e. Relationships)
MP/Scripts – Set of programmable steps/settings
Operator Assisted – User Interface or SA with prompts
Fully Automated – User Interface with SA in background running without operator required

## Slide 4: Simple Automation
SA has ample functions for automating various measurement tasks:
    Auto Measuring
    Relationships
    Pipe Fit Module
    Auto Reporting
    6 DOF Trans-Track
    Machine Calibration

## Slide 5
Initial errors
Final residuals
Group to Group Relationship

## Slide 6
Frame to Frame Relationship

## Slide 7: Pipe Fit Module - Relationships
Notes: This is where Spatial Analyzer is defining the optimal fit.
Here we have one of our steam generators attempting to fit itself to the Primary Heat Transport (PHT) piping and the steam drum. The key features are the inlet pipe, the outlet pipe and the steam drum nozzle. You can see the steam generator model wobble around with each successive iteration. The pipe fit module allowed us to not only align the pipes, but was instrumental in accounting for pipe thickness and angularity.
On the left side of the screen, you can see the program is working through the iterations and trying to arrive at the best fit solution.
By changing constraints, relationships and the weighting of certain features, SA is able to determine the machining cut planes.
Arriving at this solution could take a minute or up to 45 minutes and multiple attempts may also have to be made before arriving at the final result.

## Slide 8: Automation using Measurement Plans/Scripts
Increasing level of control of automation
SA User defines the steps and controls the level of complexity
MP is tailored to fit the application or process
Operator interaction can be highly refined
Data can be output to populate other files or to feed information into a auxiliary activity

## Slide 9: Measurement Plans in SA

## Slide 10: NIST – Neutron Guide Alignment

## Slide 11
NRK SA with MPs for process automation

## Slide 12: Operator Instructed Task
Airbus A350 Wing Jig Inspection

## Slide 13
A350 Rapid Tool Recertification
Task Definition for Automating Measurements

## Slide 15
Mini Test Jig for A350

## Slide 16: Fully Automated Aircraft Join
Fuselage Assembly of Business Jet
  Join Wings
  Join Center Fuselage to Wings
  Join Fwd / Aft to Center Section
  Align Flight Control Surfaces
Operation Must Not Require Metrologist
User Interface Will Not Show SA Screens
Joining and Measuring Tightly Integrated Between Siemens Controller and SA
Reporting/Data Storage Automated

## Slide 17: Forward/Aft Fuselage Join

## Slide 18: Join Station with Controllers

## Slide 19: Test Join AC #001

## Slide 20: Automated Workstation

## Slide 21
Global 7000 Interior During Join

## Slide 22
Automation can be as simple as defining a relationship or using an existing function
The flexibility of SA allows users to begin with existing functions and mature to develop highly efficient and capable MPs or coded programs
The level of automation is dictated by the necessity to repeat a process and the skill of the operators performing the tasks
Many of the tasks initially attempted using some of SA’s built in functions can be upgraded to either partially or fully automated measurements and alignment activities.
Final Thoughts on Automation