## Slide 1: GD&T Inspection in SpatialAnalyzer
Jeremy Winn
Application Engineer
New River Kinematics
Philip Wilson
Application Engineer
New River Kinematics

## Slide 2: GD&T Inspection
Incorporating
Standardized Inspection within SpatialAnalyzer
Notes: SA’s GD&T Inspection tools provides engineer’s the ability to perform standardized Geometric Dimensioning and Tolerancing
with complete confidence that their inspection is in accordance with the guidelines of the ASME or ISO standard.

## Slide 3: GD&T Inspection
GD&T
“Regular Inspection”
Alignments Datum Structure Current Position
Check Specific
Computation Bounding Tol. Zone RMS (root mean square)
Outlier Pts = Part Error User controls rejection rules
Goals: Pass/Fail at Tolerance Is the part good and if not..,
how do I fix it?
Notes: SA’s GD&T Inspection tools provides engineer’s the ability to perform standardized Geometric Dimensioning and Tolerancing
with complete confidence that their inspection is in accordance with the guidelines of the ASME or ISO standard.

## Slide 4: GD&T Inspection
Defining the Checks
Building Annotations
    Tolerance Structure
    Nominal designation
GD&T Inspection can be Divided into 2 Distinct Steps
Measurement Process
  Data Gathering & Association
    Inspection/ inspect scripting
    Toolkit or direction Association
    or Measurement Plan (MP)

## Slide 5: GD&T and CAD Import
Notes: To the import a CAD model with annotations use File>Import>Direct CAD Access. See Direct CAD Access for supported formats.

## Slide 6
GD&T Annotations

## Slide 7: GD&T Annotations
SA Objects/CAD Face
Datum Assignment
Tolerance Definition

## Slide 8: GD&T Annotations
Datum Annotations:
SA Objects/CAD Face

## Slide 9
Building Annotations

## Slide 10: GD&T Annotations
Annotation View Orientation:
CAD Faces vs. SA Objects
  SA Objects (Fit to Points)

## Slide 11: GD&T Annotations
Datum and Datum Target Designations
    (Hold down A-Z to pick a letter)
    Click-point defines leader line anchor point

## Slide 12: GD&T Annotations
Feature Checks Designation:

## Slide 13: GD&T Annotations
  Form Checks
    Datum Independent
  Orientation Checks
    Depend on 1 Datum
  Location Checks
    Can Include 1-3 Datums
    Can Include 1-2 Tiers
Feature Checks Designation:

## Slide 14: GD&T Annotations
Required for Material Modifiers
  MMC, LMC
Dimensional Tolerances
  Datum Independent

## Slide 15: Building Annotations Demo
Notes: Objective is to demonstrate:
Setting a view for the Annotations
Adding Datums Annotations
Adding Feature checks Annotations
Opening the Properties and changing properties
Controlling Graphical Placement
End with Direct CAD Import with all the annnotations

## Slide 16: GD&T Inspection
Defining the Checks
Building Annotations
    Tolerance Structure
    Nominal designation
GD&T Inspection can be Divided into 2 Distinct Steps
Measurement Process
  Data Gathering & Association
    Inspection/ inspect scripting
    Toolkit or direction Association
    or Measurement Plan (MP)

## Slide 17: Building Feature Checks
Tree Structure
  Annotations
    Tolerance & check definition
  Datums & Feature Checks
    Link points to annotations
    Point offset & evaluation control
    Contain guided inspection controls

## Slide 18: Building Feature Checks

## Slide 19: GD&T Inspection
Direct Point Association

## Slide 20: GD&T Inspection
Guided Inspection
Design
Rehearse
Inspect

## Slide 21: Demo- Basic Fit & Link
Notes: Objective is to demonstrate:
Setting a view for the Annotations
Adding Datums Annotations
Adding Feature checks Annotations
Opening the Properties and changing properties
Controlling Graphical Placement
End with Direct CAD Import with all the annnotations

## Slide 22: Check Details
Feature Checks come in 3 Categories:
  Orientation Checks
  Location Checks
  Form Checks

## Slide 23: Flatness
Flatness Evaluation Process within SA:
Two parallel planes are built bounding the extents of the data.
These planes are allowed to freely rotate to establish the minimum distance between them while still containing the data.

## Slide 24: Flatness
Standard Inspection (RMS):

## Slide 25: Flatness
Flatness Evaluation Process within SA:
Two parallel planes are built bounding the extents of the data.
These planes are allowed to freely rotate to establish the minimum distance between them while still containing the data.

## Slide 26: Cylindricty
Cylindricity Evaluation Process within SA:
Two coaxial cylinders are built bounding the extents of the data.
The cylinders are allowed to freely rotate to establish the minimum distance between them while still containing the data.

## Slide 27: Orientation Checks
Datum
Nominal Angle
Deviation = Distance btw Planes

## Slide 28: Surface Profile
Surface Profile Evaluation Process within SA:
An inner and outer tolerance boundary is established
The profile is allowed to rotate based on the datum constraints to minimize the deviations
The extent of the max and min deviation is used to establish the measured profile deviation

## Slide 29: GD&T Annotations
Feature Checks Categories:
Cross Section
Checks

## Slide 30: GD&T Annotations
Cross Section Checks:
Runout
Cross Section
Check
Total Runout
Surface Check

## Slide 31: Concentricity
Cross Section Checks:
Concentricity
Cross Section
Check

## Slide 32: GD&T Annotations
Cross Section
Checks

## Slide 33: Datum Alignment
Right- Click Datum Category
  Select “Align”

## Slide 34: Building Feature Checks
Cylinder Evaluation Method
Probe Compensation

## Slide 35: Datum Alignment
Datums and Degrees of Freedom
Geometry Type is the Key

## Slide 36: Datum Alignment
The number of datums specified and the feature type selected controls the degrees of freedom for the check:
SA Objects/CAD Face
SA Offset object

## Slide 37: Demo- Basic Fit & Link
Notes: Objective is to demonstrate:
Setting a view for the Annotations
Adding Datums Annotations
Adding Feature checks Annotations
Opening the Properties and changing properties
Controlling Graphical Placement
End with Direct CAD Import with all the annnotations

## Slide 38
Building Feature Checks
Inspection Controls
Evaluation Method

## Slide 39: Building Feature Checks
Cylinder Evaluation Method

## Slide 40: Building Feature Checks
Cylinder Evaluation Method

## Slide 41: Building Feature Checks
Cylinder Evaluation Method

## Slide 42: Building Feature Checks
Cylinder Evaluation Method

## Slide 43: Composite True Position
Composite Checks:

## Slide 44
Automatic Point Association
GD&T Inspection
Proximity Filter
Based on Initial
Alignment

## Slide 45
Automatic Point Association
GD&T Inspection

## Slide 46
Automatic Point Association
GD&T Inspection

## Slide 47: Reporting

## Slide 48: Reporting
Summary Table
Fit Transform
Datum Statistics
Details Table
Point Deviations

## Slide 49: Reporting
Vectors for Visualization:
Specific Alignment
DoF Understanding

## Slide 50: Reporting

## Slide 51: Reporting

## Slide 52: Evaluations Tools

## Slide 53: Thank You