## Slide 1: ALIGNMENTS: RPS and Sequential
By: Jay Urquhart

## Slide 2: JAY URQUHART
ABOUT ME
Dimensional Control Apprentice 2007-2011
Metrology Technician 2011 – 2015
New River Kinematics 2015 - Present

## Slide 3: Ribbons
SA has added Ribbons!
  NRK never stops developing-Always striving to be the best
  Continued Investment for now and the future
  SA has never been better and easier to use

## Slide 4: Ribbons
Why:
  Streamline processes/Easier to use
  Modern look and feel
  Reduces mouse clicks
  Easier access to frequently used commands
  Without loss of functionality
  Legacy Interface will remain and easily reset

## Slide 5: ALIGNMENTS
TEXT Questions to (757)-300-1774

## Slide 6: INSTRUMENT > LOCATE
Point to Point Alignments
Measure Nominal Points
Best-Fit
Nominal Geometry Relationships
RPS Alignment
Points to Objects Alignments
Quick Align to CAD
Minimizing Relationships
RPS Alignment
Frame to Frame Alignments
Frame Wizard
Frame to Frame
Cloud to Object Alignments
Align Cloud to CAD
Align Cloud to Mesh
*Sequential Alignment*

## Slide 7: NEW ALIGNMENT TECHNIQUES
RPS & Sequential Alignments
  What are they?
  What do you need to run them in SA?
  How to flow through the alignment process.

## Slide 8: RPS ALIGNMENT

## Slide 9: RPS ALIGNMENT?
Reference Point System
Uses surface points
Point reducible features
(Circles, Slots and Spheres)

## Slide 10: RPS ALIGNMENT
RPS is unique in that it provides the means to use a set of point reducible features (such as circle centers) as well as surface points to achieve an alignment.
Slot
Circle 2
Circle 1
Sphere

## Slide 11
RPS ALIGNMENT (Reference Point System Alignment)

## Slide 12
Point to reference point relationship
Allows for selection or creation projection plane
Nominal geometry circle relationship
Creates nominal geometry slot relationship
Creates nominal geometry sphere relationship
Run (re-run) Alignment Fit
Apply Alignment Fit
Undo Previous Instrument Locate
Select Existing Geometry Relationship
RPS ALIGNMENT (Reference Point System Alignment)

## Slide 13
Nominal geometry relationships can be created ahead of time or from the RPS dialog.
Visit our Part Inspection and Job Templating Sections to learn more!!
RPS ALIGNMENT (Reference Point System Alignment)

## Slide 14
RPS ALIGNMENT (Reference Point System Alignment)
Name Alignment
Choose degrees of freedom

## Slide 15
Show the advanced section for more information.
RPS ALIGNMENT (Reference Point System Alignment)

## Slide 16
Overall RelationshipWeight
Magnitude Column
Component Weights
RPS ALIGNMENT (Reference Point System Alignment)

## Slide 17
RPS ALIGNMENT (Reference Point System Alignment)
The Moving Instrument
* IF UNCHECKED, YOU WILL BE PROMPTED TO SELECT THE MOVING OBJECTS AND INSTRUMENTS WHEN THE APPLY ALIGNMENT FIT BUTTON IS SELECTED*

## Slide 18
Undo Instrument Locate
RPS ALIGNMENT (Reference Point System Alignment)

## Slide 19
Performing a Basic RPS Alignment
1. Import a CAD model into your job and add an instrument.
2. Select the RPS Alignment from the Alignment tab of the ribbon bar.
3. Build a set of surface points or point reducible features on a CAD model to define the coordinate axes.
4. Indicate how the point features will be used by checking the component check boxes
5. Press the Run Alignment Icon and check that everything is within the specified tolerance (set within the Summary Section). And then press the Apply Alignment Button to locate the instrument.
RPS ALIGNMENT (Reference Point System Alignment)

## Slide 20: RPS ALIGNMENT EXAMPLE

## Slide 21: SEQUENTIAL ALIGNMENT

## Slide 22: SEQUENTIAL ALIGNMENT?
Apply one relationship optimization after another in a specific sequence
Individual degrees of freedom can be set with each relationship or group of relationships
Uses points/group to objects relationships
Ideal to for GD&T style alignments
A
B
C

## Slide 23: SEQUENTIAL ALIGNMENT
Typical relationships types used:
Point to Point
Point to Object or CAD Faces
Object to Object Angle
Points to Objects or CAD Faces

## Slide 24: SEQUENTIAL ALIGNMENT

## Slide 25: SEQUENTIAL ALIGNMENT
Allows for selection of moving objects and instruments
Run (re-run) Alignment Fit
Select existing relationship
Apply Alignment Fit
Undo Previous Instrument Locate

## Slide 26: SEQUENTIAL ALIGNMENT
Choose desired relationships…

## Slide 27: SEQUENTIAL ALIGNMENT

## Slide 28: SEQUENTIAL ALIGNMENT

## Slide 29: SEQUENTIAL ALIGNMENT
Performing a basic Sequential Alignment
1. Select the RPS Alignment from the Alignment tab of the ribbon bar.
2. Select Existing Relationships button to select the desired relationships.
3. Select the Objects and Instruments to Move button and choose what you wish to move. (Typically instrument selection is all that is required.)
4. Rearrange the order of the relationships for the desired sequence and select the degrees of freedom you wish to influence through the relationship.
6. Select the Run (Re-Run) the Alignment Fit button to compute a fit.
7. When the numbers look good apply the fit by selecting the Apply Alignment Fit button which graphically aligns your data.
8. If necessary, the instrument can be put back in its starting position by selecting the Undo the Applied Alignment button.

## Slide 30: SEQUENTIAL ALIGNMENT EXAMPLE

## Slide 31: Alignments in the tree
RIGHT-CLICK

## Slide 32: SA User Community
Navigate to via www.kinematics.com OR Direct Access – kinematics.force.com/SA
TEXT Questions to (757)-300-1774 for closing remarks discussion